## Slide 1: GPU Architectures
Prof. Onur Mutlu
ETH Zürich
Spring 2023
11 May 2023

## Slide 2: GPUs are SIMD Engines Underneath
The instruction pipeline operates like an SIMD pipeline (e.g., an array processor)
However, the programming is done using threads, NOT SIMD instructions
Let us distinguish between
  Programming Model (Software) vs.
  Execution Model (Hardware)

## Slide 3: Programming Model vs. Hardware Execution Model
Programming Model refers to how the programmer expresses the code
  E.g., Sequential (von Neumann), Data Parallel (SIMD), Dataflow,
Multi-threaded (MIMD, SPMD), …
Execution Model refers to how the hardware executes the code underneath
  E.g., Out-of-order execution, Vector processor, Array processor,
Dataflow processor, Multiprocessor, Multithreaded processor, …
Execution Model can be very different from the Programming Model
  E.g., von Neumann model implemented by an OoO processor
  E.g., SPMD model implemented by a SIMD processor (a GPU)

## Slide 4: How Can You Exploit Parallelism Here?
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Let’s examine three programming options to exploit instruction-level parallelism present in this sequential code:
1. Sequential (SISD)
2. Data-Parallel (SIMD)
3. Multithreaded (MIMD/SPMD)

## Slide 5: Prog. Model 1: Sequential (SISD)
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Can be executed on a:
Pipelined processor
Out-of-order execution processor
Independent instructions executed when ready
Different iterations are present in the instruction window and can execute in parallel in multiple functional units
In other words, the loop is dynamically unrolled by the hardware
Superscalar or VLIW processor
  Can fetch and execute multiple instructions per cycle
for (i=0; i < N; i++)
C[i] = A[i] + B[i];

## Slide 6: Prog. Model 2: Data Parallel (SIMD)
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
load
llooaadd
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
Vector Instruction
add
ssttoorree
load
load
add
store
Itelro.ad 1
Iter. 2
Vectorized Code
VLD A  V1
VLD B  V2
VADD V1 + V2  V3
VST V3  C
Realization: Each iteration is independent
Idea: Programmer or compiler generates a SIMD instruction to execute the same instruction from all iterations across different data
Best executed by a SIMD processor (vector, array)

## Slide 7: Prog. Model 3: Multithreaded
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
load
llooaadd
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
add
ssttoorree
Itelro.ad 1
load
load
add
store
Iter. 2
Realization: Each iteration is independent
Can be executed on a MIMD machine
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)

## Slide 8: Prog. Model 3: Multithreaded
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
Can be executed on a MIMD machine
Can be executed on a SIMD machine
8
This particular model is also called:
SPMD: Single Program Multiple Data
Can be executed on a SIMT machine Single Instruction Multiple Thread

## Slide 9: A GPU is a SIMD (SIMT) Machine
Except it is not programmed using SIMD instructions
It is programmed using threads (SPMD programming model)
  Each thread executes the same code but operates a different piece of data
  Each thread has its own context (i.e., can be treated/restarted/executed independently)
A set of threads executing the same instruction are dynamically grouped into a warp by the hardware
  A warp is essentially a SIMD operation formed by hardware!

## Slide 10: Warp Terminology
Source: Wikipedia

## Slide 11: SPMD on SIMT Machine
Warp 0 at PC X+3
Warp 0 at PC X+2
Warp 0 at PC X+1
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
Can be executed on a MIMD machine
Can be executed on a SIMD machine
11
This particular model is also called:
SPMD: Single Program Multiple Data
A GPU executes it using the SIMT model: Single Instruction Multiple Thread
Warp 0 at PC X
Warp: A set of threads that execute the same instruction (i.e., at the same PC)

## Slide 12: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions 
threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently (on any type of scalar pipeline)  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 13: Fine-Grained Multithreading of Warps
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 32020*32
Iter. 21303*32 + 1
Warp 10 at PC X
Assume a warp consists of 32 threads
If you have 32K iterations, and 1 iteration/thread  1K warps
Warps can be interleaved on the same pipeline  Fine grained multithreading of warps
Warp 20 at PC X+2

## Slide 14: Fine-Grained Multithreading (FGMT) of Warps
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Warp 0 at PC X+3
Iterations 0-31
Assume a warp consists of 32 threads
If you have 32K iterations, and 1 iteration/thread  1K warps
Warps can be interleaved on the same pipeline  Fine grained multithreading of warps
Warp 1 at PC X+2
Iterations 32-63
Warp 2 at PC X+1
Iterations 64-95
Warp 3 at PC X
Iterations 96-127
All threads in a warp are independent of each other
 They be executed seamlessly in a fine-grained multithreaded pipeline

## Slide 15: Fine-Grained Multithreading: Basic Idea
SignImmE
CLK
A RD
Instruction Memory
+
4
A1
WE3 RD1
CLK
Sign Extend
A2 RD2
A3
WD3 Register
File
0
1
0
1
A RD
Data
Memory
WD
WE
0
PCF
0
1
PC'
InstrD
25:21
20:16
15:0
SrcBE
20:16
15:11
RtE
RdE
<<2
+
ALUOutM
ALUOutW
ReadDataW
1
WriteDataE
WriteDataM
SrcAE
PCPlus4D
PCBranchM
WriteRegM
4:0
ResultW
PCPlus4E
PCPlus4F
RegDstD
BranchD
MemWriteD
MemtoRegD
ALUControlD
ALUSrcD
RegWriteD
31:26 Op
5:0 Funct
Control
Unit
ZeroM
PCSrcM
CLK
CLK
CLK
CLK
CLK
WriteRegW
4:0
ALUControlE2:0
ALU
RegWriteE
RegWriteM
RegWriteW
MemtoRegE
MemtoRegM
MemtoRegW
MemWriteE
MemWriteM
BranchE
BranchM
RegDstE
ALUSrcE
WriteRegE
4:0
Each pipeline stage has an instruction from a different, completely-independent thread
We need a PC and a register file for each thread + muxes and control

## Slide 16: Warps and Warp-Level FGMT
Warp: A set of threads that execute the same instruction (on different data elements)  SIMT (Nvidia-speak)
All threads run the same code
Warp: The threads that run lengthwise in a woven fabric …
Thread Warp 3
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar Thread W | Scalar Thread X | Scalar Thread Y
Scalar Thread Z
Common PC
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.
SIMD Pipeline

## Slide 17: High-Level View of a GPU
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.

## Slide 18: Latency Hiding via Warp-Level FGMT
Warp: A set of threads that execute the same instruction (on different data elements)
Fine-grained multithreading
  One instruction per thread in pipeline at a time (No interlocking)
  Interleave warp execution to hide latencies
Register values of all threads stay
in register file
FGMT enables simple pipeline & long latency tolerance
Millions of threads operating on the
same large image/video
18
Decode
RF
RF
RF
ALU
ALU
ALU
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Warps accessing memory hierarchy Miss?
Thread Warp 3
Thread Warp 8
Writeback
Warps available for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline
Slide credit: Tor Aamodt

## Slide 19: Recall: Vector Instruction Execution
VADD A,B  C
C[1]
C[2]
A[6] | B[6] | A[24] | B[24] | A[25] | B[25] | A[26] | B[26] | A[27] | B[27]
A[5] | B[5] | A[20] | B[20] | A[21] | B[21] | A[22] | B[22] | A[23] | B[23]
A[4] | B[4] | A[16] | B[16] | A[17] | B[17] | A[18] | B[18] | A[19] | B[19]
A[3] | B[3] | A[12] | B[12] | A[13] | B[13] | A[14] | B[14] | A[15] | B[15]
Execution using one pipelined functional unit
C[4]
C[8]
C[5]
C[9]
C[6]
C[10]
C[7]
C[11]
Execution using four pipelined functional units
Time
Time
C[0]
C[0]
C[1]
C[2]
C[3]
Space
Slide credit: Krste Asanovic

## Slide 20: Warp Execution (Recall the Previous Slide)
32-thread warp executing ADD A[tid],B[tid]  C[tid]
C[1]
C[2]
A[6] | B[6] | A[24] | B[24] | A[25] | B[25] | A[26] | B[26] | A[27] | B[27]
A[5] | B[5] | A[20] | B[20] | A[21] | B[21] | A[22] | B[22] | A[23] | B[23]
A[4] | B[4] | A[16] | B[16] | A[17] | B[17] | A[18] | B[18] | A[19] | B[19]
A[3] | B[3] | A[12] | B[12] | A[13] | B[13] | A[14] | B[14] | A[15] | B[15]
Execution using one pipelined functional unit
C[4]
C[8]
C[5]
C[9]
C[6]
C[10]
C[7]
C[11]
Execution using four pipelined functional units
Time
Time
C[0]
C[0]
C[1]
C[2]
C[3]
Space
Slide credit: Krste Asanovic

## Slide 21: Recall: Vector Unit Structure
Lane
Functional Unit
Partitioned
Vector
Registers
Elements 0, 4, 8, …
Memory Subsystem
Slide credit: Krste Asanovic
Elements 1, 5, 9, …
Elements 2, 6, 10,
…
Elements 3, 7, 11,
…

## Slide 22: GPU SIMD Execution Unit Structure
Lane
Functional Unit
Registers for each Thread
Registers for thread IDs 0, 4, 8, …
Registers for thread IDs 1, 5, 9, …
Registers for thread IDs 2, 6, 10, …
Registers for thread IDs 3, 7, 11, …
Memory Subsystem
Slide credit: Krste Asanovic

## Slide 23: SIMT Memory Access (Loads and Stores)
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
+
Same instruction in different threads uses thread id to index and access different data elements
Let’s assume N=16, 4 threads per warp  4 warps
Threads
+
+
+
+
Data elements
(i.e., elements per cycle throughput to match computation unit throughput)
25
Slide credit: Hyesoon Kim
Warp 0 Warp 1 Warp 2 Warp 3
For maximum performance, memory should provide enough bandwidth

## Slide 24: Warps not Exposed to GPU Programmers
CPU threads and GPU kernels
  Sequential or modestly parallel sections on CPU
  Massively parallel sections on GPU: Blocks of threads
Serial Code (host)
. . .
. . .
Parallel Kernel (device)
KernelA<<<nBlk, nThr>>>(args);
Serial Code (host)
Parallel Kernel (device)
KernelB<<<nBlk, nThr>>>(args);
26
Slide credit: Hwu & Kirk

## Slide 25: Sample GPU SIMT Code (Simplified)
CPU code
for (ii = 0; ii < 100000; ++ii) {
C[ii] = A[ii] + B[ii];
}
CUDA code
// there are 100000 threads
global void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x; int varA = aa[tid];
int varB = bb[tid]; C[tid] = varA + varB;
}
Slide credit: Hyesoon Kim

## Slide 26: Sample GPU Program (Less Simplified)
Slide credit: Hyesoon Kim

## Slide 27: From Blocks to Warps
GPU core: A SIMD pipeline
  Streaming Processor (SP)
  Many such SIMD Processors
    Streaming Multiprocessor (SM)
Blocks are divided into warps
  SIMD/SIMT unit (32 threads)
…
Block 0’s warps
…
t0 t1 t2 … t31
…
Block 1’s warps
…
t0 t1 t2 … t31
…
Block 2’s warps
…
t0 t1 t2 … t31
NVIDIA Fermi architecture

## Slide 28: Warp-based SIMD vs. Traditional SIMD
Traditional SIMD contains a single thread
  Sequential instruction execution; lock-step operations in a SIMD instruction
  Programming model is SIMD (no extra threads)  SW needs to know
vector length
  ISA contains vector/SIMD instructions
Warp-based SIMD consists of multiple scalar threads executing in a
SIMD manner (i.e., same instruction executed by all threads)
  Does not have to be lock step
  Each thread can be treated individually (i.e., placed in a different warp)
 programming model not SIMD
    SW does not need to know vector length
    Enables multithreading and flexible dynamic grouping of threads
  ISA is scalar  SIMD operations can be formed dynamically
  Essentially, it is SPMD programming model implemented on SIMD
hardware

## Slide 29: SPMD
Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g. barriers
Essentially, multiple instruction streams execute the same program
  Each program/procedure 1) works on different data, 2) can execute a different control-flow path, at run-time
  Many scientific applications are programmed this way and run on MIMD
hardware (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD hardware

## Slide 30: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions 
threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently on any type of scalar pipeline  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 31: Threads Can Take Different Paths in Warp-based SIMD
Each thread can have conditional control flow instructions
Threads can execute different control flow paths
Thread Warp | Common PC
Thread 1 | Thread 2 | Thread 3 | Thread 4
C
Slide credit: Tor Aamodt
D
F
A
B
E
G

## Slide 32: Control Flow Problem in GPUs/SIMT
A GPU uses a SIMD pipeline to save area on control logic
  Groups scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths
Branch
Path A
Path B
Branch
Path A
Path B
This is the same as conditional/predicated/masked execution. Recall the Vector Mask and Masked Vector Operations
Slide credit: Tor Aamodt

## Slide 33: Remember: Each Thread Is Independent
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently on any type of scalar pipeline  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing
If we have many threads
We can find individual threads that are at the same PC
And, group them together into a single warp dynamically
This reduces “divergence”  improves SIMD utilization
  SIMD utilization: fraction of SIMD lanes executing a useful operation (i.e., executing an active thread)

## Slide 34: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction, i.e., at the same PC (after branch divergence)
Form new warps from warps that are waiting
  Enough threads branching to each path enables the creation of full new warps
Warp X Warp Y
Warp Z

## Slide 35: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction, i.e., at the same PC (after branch divergence)
Fung et al., “Dynamic Warp Formation and Scheduling for Efficient GPU Control Flow,” MICRO 2007.
Branch
Path A
Path A
Path B
Branch

## Slide 36: Dynamic Warp Formation Example
38
Time
A A B B
G G A A
C D
E E
F
Time
A x/1111
y/1111
B x/1110
y/0011
C x/1000 D x/0110
y/0010 y/0001
F x/0001
y/1100
E x/1110
y/0011
G x/1111
y/1111
A A B B C C D D E E F F G G A A
Legend
A A
Execution of Warp x Execution of Warp y
at Basic Block A at Basic Block A
D
A new warp created from scalar threads of both Warp x and y executing at Basic Block D
Baseline
Dynamic Warp Formation
Slide credit: Tor Aamodt

## Slide 37: Large Warps and Two-Level Warp Scheduling
40
time
Memory System
Core All Warps Compute
All Warps Compute
Req Warp 0
Req Warp 1
Req Warp 15
Round Robin Scheduling, 16 total warps
Two main reasons for GPU resources be underutilized
  Branch divergence
  Long latency operations
Long-latency load
Narasiman et al., “Improving GPU Performance via Large Warps and Two-Level Warp
Scheduling,” MICRO 2011.

## Slide 38: Two-Level Scheduling of Warps
Scheduling smaller warp groups reduces stalls due to long latency operations
time
Memory
System
Core All Warps Compute
All Warps Compute
Req Warp 0
Req Warp 1
Req Warp 15
Round Robin Scheduling, 16 total warps
time
Memory System
Req Warp 0
Req Warp 1
Req Warp 7
Two Level Round Robin Scheduling, 2 fetch groups, 8 warps each
Narasiman et al., “Improving GPU Performance via Large Warps and Two-Level Warp Scheduling,” MICRO 2011.
Req Warp 8
Req Warp 9
Req Warp 15
Group 0 Group 1 Group 0 Group 1
Core Compute Compute Compute Compute
Saved Cycles

## Slide 39: Why Ai boost GPUs Era
Massive linear‑algebra workloads – every training step is just huge GEMMs and convolutions; GPUs already had thousands of FP/INT lanes built for graphics.
Data & model sizes exploded – GPT‑2 (2019) ≈ 110 M params → GPT‑4‑class (2023) ≈ 1.8 T params; FLOP demand grew 2‑3 × per year, far faster than CPU cores.
Energy / $ efficiency – H100 delivers ≈ 1.5 PFLOP FP16 per board at ~700 W; a CPU cluster needs 10× the racks (and power) for the same math [megware](see pdf).
CUDA / ROCm software moat – mature kernels, automatic kernel fusion, graph compilers (TensorRT, TVM, XLA) let researchers stay productive while hardware evolves.

## Slide 40: Self Attention in LLM and Transformer
Core op: Q × Kᵀ → Softmax → (result) × V; three dense GEMMs dominate the FLOPs.
Parallel axes everywhere – batch B, heads h, sequence length N, hidden dim d → ideal for 2‑D/3‑D thread‑block tiling.
Sequence‑length bottleneck: O(N²) compute & memory; GPUs hide that with huge SRAM tiles + warp‑specialized kernels (FlashAttention, xFormers).
Hopper’s Transformer Engine automatically chooses FP8/FP16 and kicks in fused‑QKV kernels.

## Slide 41: Self Attention in LLM and Transformer
Self-Attention and Transformer Network Architecture | by LM Po | Medium

## Slide 42: Self Attention in LLM and Transformer
A query represents what you’re looking for.
Keys represent identifiers or tags associated with pieces of information (documents, words, etc.).
Values represent the actual content or information that you want to retrieve.

## Slide 43: Step by step computations
Compute the Query, Key, and Value Matrices: First, we transform each token of our sentence into three different vectors Q, K, and V. This is done by multiplying the input embeddings with learned weight matrices.

## Slide 44: Step by step computations
Calculate Attention Scores: Next, we calculate how much each word should pay attention to every other word by taking the dot product of the Query and Key matrices.

## Slide 45: Step by step computations
Scaling the Scores: To mitigate the problem of large variance in high-dimensional matrices, the dot products are scaled by the square root of the dimensionality of Key vectors (√dₖ).

## Slide 46: Step by step computations
Apply the Softmax Function: The scaled scores are passed through a softmax function to normalize the values between 0 and 1.

## Slide 47: Step by step computations
Weight the Values: The attention weights are used to compute a weighted sum of the value matrix, resulting in the final output of the self-attention mechanism.

## Slide 48: Example

## Slide 49: Tensor Core Architecture

## Slide 50: Tensor Core Architecture

## Slide 51: MMA(Matrix Multiply Accumulate ) Unit

## Slide 52: MMA(Matrix Multiply Accumulate ) Unit
Systolic Array Concept
A systolic array is a grid (or network) of simple processing elements that rhythmically pass data between each other in a way that mimics the pumping of blood (hence “systolic”). It’s like a conveyor belt where each element performs a small computation and then passes the intermediate result along.

## Slide 53: MMA(Matrix Multiply Accumulate ) Unit
How It Works:
Data Flow: Each processing element in the array performs a multiply-accumulate (or a simpler operation) and sends the output to the next neighbor. This creates a “wave” of operations that moves across the array.
Pipelining: The structure is highly pipelined, which means that while one part of the array is doing multiplication, another may be adding the previous results, thus achieving parallelism and high throughput.
Data Reuse: Since data is passed from one processing element to the next, there's less need to move data back and forth from slower memory, which reduces latency and improves overall efficiency.